## Slide 1: Designing the Snake Game on Basys-3 with VGA and Joystick Pmod
Huu Nhan Nguyen, Julia Gu
CS M152A

## Slide 2: Demo
Joystick:
Supports four directions
Does not allow backward movement
Game logic:
Start and reset buttons drive states
Collisions with wall or self lead to loss screen
Length of snake increments after collecting a target
Loss screen shows final target count

## Slide 3: Challenges
Connection between Basys 3 board with joystick and VGA
The snake could only turn every other cell
  Source of bug
    Snake’s refresh rate was faster than joystick’s send/receive rate
    Program did not receive joystick input in time to turn

## Slide 4
Special thanks!
    Melissa’s group for link to VGA starter code
    Ruining for link to joystick starter code
Solution
    Increased send/receive rate to twice snake’s refresh rate

## Slide 5: Design
START
RESET
BTNC
LOST
PLAY
LOST
RESET
BTNU
UP
LEFT
RIGHT
DOWN
BTND
BTNR
BTNL
BTNL
BTNR
BTND
BTNU
BTNU
BTND
BTNR
BTNL
X
Y
↓ Master_state_machine
↓ Navigation_state_machine
↓ PmodJSTK
Notes: These are some diagrams for a very small subset of our design. We have two main finite state machines and a helpful visual for how we got four directions from our joystick input.
This first one is our master state diagram. You probably saw from our demo that we had three states in our program. There was the start state, the play state, and the loss state, and these are the transitions.
The second one is our state diagram for the directions of the snake. What’s important is that there are no arrows directly between UP and DOWN, or LEFT and RIGHT, because the snake cannot go directly from up to down, or from left to right.
The third one is a visual representation of our joystick. Each trapezoid corresponds to a direction signal. We used the values of X and Y to determine which region the joystick input fell in.

## Slide 6: Modules (by theme)
Top module
  snake_wrapper
Game logic
  Master_state_machine
  Snake_control
  Navigation_state_machine
  random_num_gen
  Generic_Counter
VGA
  VGA_module
  Generic_Counter
Joystick
  PmodJSTK_Demo
  PmodJSTK
  spiCtrl
  SPImode0
  ClkDiv_5Hz
  ClkDiv_66_67kHz

## Slide 7: Q&A

## Slide 8: Modules (hierarchy)
snake_wrapper
  Master_state_machine
  Snake_control
    Generic_Counter
  Navigation_state_machine
  random_num_gen
  VGA_module
    Generic_counter
  PmodJSTK_Demo
    PmodJSTK
      spiCtrl
      SPImode0
      ClkDiv_66_67kHz
    ClkDiv_5Hz